## Slide 1
FLEET NETWORK TESTING
Network Testing at Fleet Scale
iperf_orchestrator · matrix_orchestrator · netmesh
and reachable, keeping the server list honest
Martin Gallagher

## Slide 2
OVERVIEW
Three questions, three tools
Network Testing at Fleet Scale
2
Testing a fleet's network really means answering three different questions — each tool here answers one of them.
Tool | The question it answers | Network state | Cost to run
netmesh | Is the network healthy, and which link is sick? — RTT, jitter, loss, path MTU | Idle — the baseline | ~10 small pkts/s per pair; safe on production
iperf_orchestrator | How much TCP bandwidth can every link carry, all at once? | Fully loaded | Line-rate flood — schedule a window
matrix_orchestrator (mx) | How many packets/sec can the fleet exchange, when every packet is answered? | Loaded at the rate you choose | Tunable, gentle → torture
They're one family: the same servers.txt, the same ssh-only model, and grids that read the same way. And they measure different layers of the same fabric — a 9.4 Gbit/s result over a 300 µs path and one over a 42 ms path are *different results*.
Notes: The frame for the whole talk. Bandwidth, packet rate and latency fail independently, so no single tool can tell you the network is fine. netmesh is cheap enough to run during an incident; iperf_orchestrator is the scheduled stress test; mx is the request/response rate test that looks like real RPC and storage traffic. Because they share one host-list grammar and one deployment model, learning one means you know how to drive all three.

## Slide 3
OVERVIEW
Why these tools
Network Testing at Fleet Scale
3
▪ They go anywhere you can ssh. No agents, no daemons, no root — nothing installed on the servers, and clean removes every trace afterwards.
▪ The numbers are honest. Blank never means zero, and the headline is what the *receiver* counted — not what the sender hoped. When a tool becomes its own bottleneck, it says so.
▪ They're one file each. Stdlib-only Python — pip install it, or just scp the file and run it.
▪ Each stands alone. Pick whichever answers today's question — no setup or ordering ties them together. They do share the same server-list format and the same verbs, so learning one means you can drive them all.
Notes: The alternative is a week of hand-run iperf, ad-hoc pssh loops, and numbers nobody trusts. Each tool is complete on its own — grab the one that matches the question in front of you. The shared conventions are a convenience, not a dependency: one servers.txt works everywhere, and the gen / start / status / summarize / stop / clean verbs mean the muscle memory transfers.

## Slide 4
OVERVIEW
reachable — the run survives dead servers
Network Testing at Fleet Scale
4
▪ Server lists rot — and a fan-out that silently skips eleven dead hosts looks exactly like one that ran everywhere.
▪ reachable prod.txt -i pings and ssh's every entry and comments out the failures, with the reason and date. When a host comes back, the next run uncomments it — and your own comments are never touched, so it's safe on cron.
▪ ssh is the gate, ping is the explanation: a host that answers ssh is kept even when ICMP is blocked.
web01
# db07 #[unreachable] pings but ssh does not answer - 2026-08-15
# ghost #[unreachable] name does not resolve - 2026-08-15
noicmp # ICMP blocked here by policy <- kept: ssh works
▪ Belt and braces: the orchestrators also fail open (--keep-going), so one dead box never aborts a 100-host run.
Notes: This answers "can the test still run when several servers are down?" — twice over. First, prune: reachable keeps the list true, distinguishes a key problem from a dead box (auth / refused / dns / no-route / timeout / down), and converges instead of decaying. Second, the tools themselves tolerate failures mid-run: per-host failures are reported and skipped, not fatal. reachable prod.txt -i before every big run is the habit to sell.

## Slide 5
PART 1
iperf_orchestrator

## Slide 6
IPERF_ORCHESTRATOR
What it is — and why you'd run it
Network Testing at Fleet Scale
6
▪ Takes iperf — the standard tool for measuring how fast the network really is between two machines — and runs it between every pair of servers in a fleet, at the same time.
▪ The point is to load the network as *efficiently as possible*: every link, both directions, simultaneously. Ten seconds of that answers the real question — what can this fabric actually carry, and what breaks first?
▪ Why run it: accept a new fabric or a change window; find the slow links and slow hosts; get a quick "is the fleet's network healthy?" picture.
▪ One command in → four artifacts out: results CSV · per-host CPU summary · pivot table · heatmap.
▪ One self-contained script, driving everything over ssh — the servers need nothing but iperf itself. A dead host is reported and skipped, never fatal.
▪ What it leaves to its siblings: latency and packet rate (that's netmesh and mx).
Notes: Lead with the goal, not the implementation: a mesh of N hosts has N·(N−1)/2 pairs, and the only way to truly max out a fabric in a short window is to orchestrate all of them at once — that's the tool's whole reason to exist. Mention only in passing that it happens to be a single script; what matters is that servers need zero setup beyond iperf and an ssh key.

## Slide 7
IPERF_ORCHESTRATOR
What is iperf?
Network Testing at Fleet Scale
7
iperf is the de-facto standard throughput tool: it fills the pipe between two machines and reports what actually got through — the true end-to-end capacity of that path: NICs, kernel, cables, switches, everything in between.
CLIENT
iperf -c <server>
SERVER
iperf -s
bytes, as fast as TCP will go
full-duplex: traffic back at the same time
run for 10 seconds → the achieved rate is the answer
Knob | What it means
duration (-t) | how long the push lasts — 10 s default; longer smooths out bursts
parallel streams (-P) | several TCP connections at once — one stream often can't fill a fat pipe
full-duplex | both directions at the same time, on one connection — like real traffic
TCP vs UDP | TCP measures achievable throughput; UDP sends a fixed rate to measure loss
Given enough CPU, iperf saturates a 1G / 10G / 25G link. But it thinks in pairs — it has no idea a fleet exists. That's the orchestrator's job.
Notes: Take a beat here for anyone who hasn't used iperf. The mental model: it answers "how fast is the pipe between A and B, really?" by filling it. Emphasize that the number includes the whole path — a slow result can be the NIC, the host's CPU, or the network, which is exactly why the orchestrator also samples CPU. The pair-at-a-time limitation is the segue to the next slide.

## Slide 8
IPERF_ORCHESTRATOR
Why iperf2 — and why an orchestrator at all
Network Testing at Fleet Scale
8
▪ Two iperfs exist: iperf2 serves many clients on one port; iperf3 takes one at a time — unusable in a mesh. iperf2's --full-duplex also tests both directions on one connection.
8 hosts 28 pairs
100 hosts 4,950 pairs
every pair both directions, at once
Making the mesh efficient | How
Everyone starts together | one "start at" timestamp pushed to all hosts — they fire within a fraction of a second
Work is spread fairly | every host runs ~half the client jobs (49–50 each at N=100, not 0–99)
Results come home fast | one archive per host, not thousands of copies — minutes instead of ~80
CPU sampled everywhere | a throughput number without CPU next to it gets misread
Notes: Each of these was a real problem hit and fixed — the tool is the accumulated answers. Worth a warning: some distros ship "iperf" as a symlink to iperf3; the check-iperf preflight catches that (WRONG_VERSION). The parity rule detail if asked: for pair {i, j}, the client is the smaller index when i+j is even, the larger when odd — both ends compute it independently, so no coordination is needed.

## Slide 9
IPERF_ORCHESTRATOR
Running it, start to finish
Network Testing at Fleet Scale
9
iperf-orchestrator --servers servers.txt all
start-servers
iperf comes up everywhere
→
run-tests
the synchronized mesh
→
collect-results
logs come home
→
process
CSV, pivot, heatmap
→
stop + cleanup
leave no trace
▪ Every run lands in its own timestamped folder — results/<run-id>/, with results/latest pointing at the newest. Old runs can be re-analyzed any time (--run-id).
▪ Reading a run, in order: ① the heatmap — a red *row* means that server sends slowly to everyone; a red *column* means everyone struggles to reach it. ② the CPU summary — if a "slow" host's CPU was pegged, you measured the host, not the network. ③ results-summary — percentiles plus the five slowest pairs.
▪ Useful switches: --dry-run (show what would run, run nothing) · --keep-going (finish past a dead host) · --resume (pick up an aborted run) · --duration / -P (longer or multi-stream tests). Every switch is also an environment variable.
Notes: Keep this non-specialist: one command does the whole pipeline, and each box in the flow is also a standalone subcommand for day-2 work — re-render a heatmap, re-collect from one host, re-run just the analysis. The reading order matters more than any switch: heatmap for *where*, CPU for *whether to believe it*, summary for *how bad*. Narration extras if asked: collection is batched one archive per host, and the remote directory is safe on shared filesystems because every file embeds host + run-id.

## Slide 10
IPERF_ORCHESTRATOR
The four run modes
Network Testing at Fleet Scale
10
Every run answers "how fast?" — the mode decides *how much traffic shares the wire at once*. That one choice trades realism against isolation against wall-clock time.
Mode | On the wire at once | @ 100 hosts | In one line
parallel (default) | everything | ~1 min | the stress test — load it all, see what breaks
sequential-host | one host's tests | ~17 min | what is each *server* capable of?
sequential-pair | one connection | ~14 h | the microscope — cleanest possible pair numbers
rolling | a few per host, continuously | you choose | fleets too big to mesh; long soaks
Notes: Frame it as one dial, four positions. parallel is realism: everything contends, like a bad day in production. The sequential modes buy isolation with time. rolling gives up the synchronized snapshot entirely in exchange for a constant, gentle load that works at any fleet size. The next four slides take them one at a time.

## Slide 11
IPERF_ORCHESTRATOR
parallel — the stress test (default)
Network Testing at Fleet Scale
11
What happens | after a synchronized start, every host fires all of its tests at once — the whole fabric is under full bidirectional load within a second
When to use it | accepting a new fabric, validating a change window — "what breaks under full load?"
How | iperf-orchestrator --servers servers.txt all
Wall-clock | ~1 test duration, at any fleet size (~50 s at N=100)
Reading the results | numbers below line rate are *normal* — every pair is sharing. Look for outliers: dark rows/columns, and hosts whose CPU pegged. Finds congestion and weak links; not any single pair's clean maximum
Notes: This is the mode the tool was built for and the one to demo. Set expectations about the numbers: under full contention a 10G host talking to 49 peers won't show 10G to each — you're reading the *distribution* and its outliers, not absolute line rate. If something looks bad here, the next two modes are how you isolate it.

## Slide 12
IPERF_ORCHESTRATOR
sequential-host — one server at a time
Network Testing at Fleet Scale
12
What happens | each host in turn runs all of its tests while every other host stays quiet
When to use it | "what is this *server* capable of?" — the follow-up for a host that looked bad under parallel
How | iperf-orchestrator --servers servers.txt all sequential-host
Wall-clock | ~N × duration (~17 min at N=100)
Reading the results | with the fabric to itself, each host should approach line rate. Still slow = a *local* problem (NIC, driver, CPU). Fine alone but bad in parallel = contention; bad in both = the host
Notes: The parallel/sequential-host comparison is the diagnostic one-two punch: the first finds the suspect, the second tells you whether it's the host or the fabric. This is also the mode for baselining what "good" looks like per host class before a stress run.

## Slide 13
IPERF_ORCHESTRATOR
sequential-pair — the microscope
Network Testing at Fleet Scale
13
What happens | exactly one connection on the wire at any moment, pair after pair
When to use it | confirming a single suspect pair with the cleanest number possible — almost never a whole fleet
How | iperf-orchestrator --servers suspects.txt all sequential-pair — list only the suspects
Wall-clock | N(N−1)/2 × duration: ~14 h at N=100, a minute at N=4
Reading the results | as clean as pair numbers get. Still slow here = the *path itself* — hand it to netmesh paths to find the hop
Notes: The trap to warn about: running sequential-pair across a big fleet because it's "the accurate one". It is — and it's quadratic. The right use is surgical: three or four hosts you already suspect, cleanest numbers in minutes, then escalate to path-level tools if it's still slow.

## Slide 14
IPERF_ORCHESTRATOR
rolling — fleets too big to mesh
Network Testing at Fleet Scale
14
What happens | no grand schedule — each host keeps a couple of short tests running against its *least-tested* peer, for as long as you budget
When to use it | very large fleets, where even the parallel mesh becomes the problem; long soak tests
How | iperf-orchestrator --total-time 1800 --flows 2 all rolling
Wall-clock | exactly the budget you give it; per-host load is constant at any fleet size
Reading the results | a survey, not a snapshot — coverage evens out over time. Read percentiles and slowest pairs; give every pair a few visits
Notes: The contrast to land: parallel is one synchronized photograph of the fleet under maximum load; rolling is a long exposure at gentle, constant load. At 1,000 hosts a full mesh is half a million pairs — rolling is the only shape that stays sane there, and its per-host load being independent of fleet size is the property that makes it safe.

## Slide 15
IPERF_ORCHESTRATOR
Tutorial — your first run
Network Testing at Fleet Scale
15
# 0. install on the machine you'll drive from
# (servers need only iperf2 + your ssh key)
pip install iperf-orchestrator
# 1. list your servers, one per line
printf '%s\n' 10.0.0.10 10.0.0.11 10.0.0.12 10.0.0.13 > servers.txt
# 2. make key-based ssh work everywhere
for h in $(grep -v '^#' servers.txt); do ssh-copy-id "$h"; done
# 3. preflight: local deps, then iperf2 + mpstat on every host
iperf-orchestrator doctor
iperf-orchestrator --servers servers.txt check-iperf
# 4. the whole pipeline, default (parallel) mode
iperf-orchestrator --servers servers.txt all
▪ You'll watch the five stages run; per-host warnings are printed but don't stop the run. A few minutes later the results directory is announced.
Notes: This and the next slide are the take-home reference. If demoing live, four small VMs are plenty. The two preflights catch ninety percent of first-run failures: missing local python packages, iperf secretly being iperf3, mpstat absent, or a host that still wants a password.

## Slide 16
IPERF_ORCHESTRATOR
Tutorial — reading it, and running it again
Network Testing at Fleet Scale
16
ls results/latest/ # iperf_results.csv cpu_summary.csv
# iperf_pivot.txt iperf_heatmap.png
iperf-orchestrator results-summary # P50/P95 + 5 slowest pairs
iperf-orchestrator --duration 30 -P 4 all # longer tests, 4 streams each
iperf-orchestrator --run-id <id> make-heatmap # re-render an old run
iperf-orchestrator --servers servers.txt cleanup --yes # tidy the servers
rows = sender · columns = receiver
A red row — that host sends slowly to everyone: its outbound is sick.
A red column — everyone struggles to reach it: its inbound is sick.
Check cpu_summary.csv before blaming the network — a pegged host makes its own links look slow.
▪ Every run is a timestamped folder: keep them, and diff results across change windows.
Notes: The habits to leave the audience with: heatmap → CPU → summary, in that order; bump --duration and -P when a single 10-second stream can't fill the pipe (common on 25G+); and treat run folders as records — the before/after diff across a change window is often the most valuable artifact the tool produces.

## Slide 17
PART 2
matrix_orchestrator (mx)

## Slide 18
MATRIX_ORCHESTRATOR
The question iperf can't answer
Network Testing at Fleet Scale
18
▪ iperf measured bytes per second. But most real traffic is *conversations* — RPCs, storage reads, control planes: a small request out, an answer back — and that stresses a network in packets per second, which is where fabrics and NICs actually fall over.
▪ mx runs exactly that shape between every pair of hosts, at a rate you choose — and the asymmetry it creates (tiny requests, fat replies) is usually what breaks first.
HOST A
mx agent
HOST B
mx agent
request: 128 bytes · 20,000 per second
reply: 8 KB — one per request, carrying its timestamp back
same packet rate both ways · 64× the bytes on the reply path · RTT for free
Notes: Land the contrast with a picture in words: a fabric can move 100 gigabits of bulk TCP happily and still collapse at two million answered packets per second — and your database traffic looks like the second thing, not the first. If asked why UDP: TCP would quietly merge small packets together, so a "packets per second" number over TCP would be fiction. The two tools are two halves of the load story: iperf_orchestrator for bytes, mx for packets.

## Slide 19
MATRIX_ORCHESTRATOR
What it does — and where it stops
Network Testing at Fleet Scale
19
▪ Does: a paced request/response matrix between every pair — rate, sizes and port all in one editable file.
▪ Does: honest accounting — the headline is what the *receivers* counted, and loss is split into the outbound leg and the return leg.
▪ Does: true round-trip percentiles per flow, and it reports its own CPU cost right next to the network numbers.
▪ Doesn't: TCP — that's iperf_orchestrator's job.
▪ Doesn't: one-way delay — that would need synchronized clocks nobody has, so it refuses to fake it.
▪ Doesn't: more than a few million packets/sec per host — beyond that you're in kernel-bypass territory. And when the tool itself becomes the limit, it tells you so rather than letting you blame the network.
Notes: The theme is honesty: receiver-counted delivery, split loss, refusal to report numbers that can't be true, and self-awareness about its own ceiling. That last one matters most in practice — a load generator that silently saturates makes the network look guilty; this one names itself and names the fix (more workers, more streams, or more hosts).

## Slide 20
MATRIX_ORCHESTRATOR
Six commands drive it
Network Testing at Fleet Scale
20
Command | What it does
mx gen | build the traffic matrix from your server list
mx start | copy the agent everywhere and start it
mx status | one live line per host — running, and how fast?
mx summarize | collect reports → pps / loss / latency + *what to do next*
mx stop | stop the agents — reports stay on the hosts
mx clean | stop, delete every trace, and verify it's gone
mx run --for 60 does the whole cycle in one shot. Servers need nothing but Python and your ssh key — no iperf, no packages, no root.
Notes: Deliberately simpler than iperf_orchestrator: six verbs and one file. Also worth naming the helpers — mx doctor checks the fleet is ready, mx check asks "can the NICs even carry what you're about to request?", and mx hints turns a goal ("2 million packets per second per host") into the exact command.

## Slide 21
MATRIX_ORCHESTRATOR
One file describes the traffic — edit it, even mid-run
Network Testing at Fleet Scale
21
# rows send, columns receive, cells are packets/sec
# tx_size=64 rx_size=512 port=5300
src\dst,10.0.0.10,10.0.0.11,10.0.0.12
10.0.0.10,,20000,20000
10.0.0.11,5000,,max
10.0.0.12,20000,20000,
▪ Everything about the traffic lives in matrix.csv — no flags to remember or re-type.
▪ Want to change a running test? Edit the file, `mx start` again. Blank a cell to silence a pair · raise a cell to make a hot pair · write max to run one pair unpaced · edit the header to reshape every packet.
▪ "What if only the cross-rack pairs run?" is a thirty-second text edit, not a feature request.
Notes: This is the tool's real interface, and the mid-stream story: investigations are edits. Agents redeploy in seconds and reports keep accumulating, so iterating on the traffic shape mid-session is normal, not exceptional.

## Slide 22
MATRIX_ORCHESTRATOR
Reading the summary
Network Testing at Fleet Scale
22
REQUESTS 2.640 Mpps what the senders put on the wire
DELIVERED 2.601 Mpps what the receivers actually counted
LOSS 1.59% round trip (1.48% outbound, 0.11% coming back)
RTT avg 240us worst flow p99 4.1ms
▪ DELIVERED is the headline — a sender can't see its own drops.
▪ Loss is split by direction — dropping tiny requests and dropping big replies point at different problems.
▪ The summary ends with WHAT TO DO NEXT — it reads its own numbers and names the knob they point at.
▪ Watch the agent CPU column: near 100% means the tool is the bottleneck, not your network — add workers (--workers), spread with --streams, or add hosts. The summary says this in as many words.
▪ mx summarize --grid g writes N×N grids: a dark row is a sick sender, a dark column a sick receiver — read exactly like the iperf heatmap.
Notes: Rule of thumb for the room: believe what arrived, not what was sent — then check whether the tool itself was working too hard before blaming the fabric. The performance model in one breath: roughly 200k packets/sec per worker process per core, times workers, times hosts; mx hints does that arithmetic for you.

## Slide 23
MATRIX_ORCHESTRATOR
Finding the fleet's limit
Network Testing at Fleet Scale
23
mx check --nic-gbps 25 # was what you're asking even possible?
mx gen --servers s.txt --pps 50000 && mx run --for 120
mx gen --servers s.txt --pps 100000 && mx run --for 120
... # raise until delivery stops keeping up
▪ The last rate that delivers cleanly is the fleet's sustainable packet rate.
▪ Two warning signs, in the order they appear: ① p99 latency lifts away from the median — queues are filling; ② DELIVERED falls behind REQUESTS — something is now dropping.
▪ In a hurry? --pps max sends unpaced and finds the ceiling fastest — but tells you less about where the comfortable limit is.
Notes: Queues fill before packets drop, so latency is the early warning — that ordering is the one thing to remember from this slide. Run mx check first so you never spend an afternoon discovering you asked a 10G NIC for 25G of replies.

## Slide 24
MATRIX_ORCHESTRATOR
Big fleets
Network Testing at Fleet Scale
24
▪ Small fleet? The default full mesh is perfect — every pair, all the time.
▪ Big fleet? --peers 8: each host talks to exactly 8 shuffled peers instead of all N−1. Every host still carries identical load, the whole fabric is still exercised — with 8 connections per host instead of hundreds.
▪ Still need every pair checked? Add --dwell 60: the 8 peers rotate on a schedule until every pair has been measured — per-host load never changes, and no coordination traffic is needed.
▪ Don't want to think about any of this? `mx hints` — tell it your goal, it prints the command.
Notes: The intuition without the math: a random 8-peer assignment already spreads load evenly and crosses every layer of the fabric — the full mesh isn't needed for equal load, only for complete pair coverage, and the rotation buys that back at the same cost. A thousand-host fleet gets every-pair coverage every few minutes on eight sockets per host. The construction is seeded and replayable if anyone asks.

## Slide 25
MATRIX_ORCHESTRATOR
Tutorial — your first mx run
Network Testing at Fleet Scale
25
# 0. install on the machine you drive from
# (servers need only python3 + your ssh key)
pip install matrix-orchestrator
# 1. servers, one per line
printf '%s\n' 10.0.0.10 10.0.0.11 10.0.0.12 > servers.txt
# 2. preflight the fleet: ssh, python, file-descriptor limits
mx doctor
# 3. describe the traffic: every pair, 20k requests/sec
mx gen --servers servers.txt --pps 20000
# 4. sanity-check it against the hardware
mx check --nic-gbps 10
# 5. run for 60 seconds: deploy, run, summarize, stop
mx run --for 60
▪ The summary prints totals, the worst hosts and flows, and what to do next.
Notes: Same shape as the iperf_orchestrator tutorial on purpose: list, preflight, one command. For a live demo three small VMs are enough — and mx selftest-style confidence comes from mx doctor plus a tiny --pps first run.

## Slide 26
MATRIX_ORCHESTRATOR
Tutorial — watching, tuning, cleaning up
Network Testing at Fleet Scale
26
mx status --watch 5 # live ticker while it runs
mx summarize # anytime -- reports accumulate
mx summarize --grid g # N x N grids for a spreadsheet
vi matrix.csv && mx start # change the traffic mid-flight
mx gen --servers servers.txt --pps 50000 && mx run --for 120 # ramp up
mx logs # keep the agent logs
mx stop # pause -- reports stay on hosts
mx clean # done -- delete every trace, verified
▪ stop and clean are different on purpose: stop keeps the evidence, clean removes it and *proves* it's gone.
▪ Everything on a server lives in one directory — no packages, no services, nothing to un-install.
Notes: The workflow to model: run, summarize, edit the matrix, run again — an investigation loop measured in seconds. Collect logs and summaries before clean; after clean there is genuinely nothing left, which is the point.

## Slide 27
PART 3
netmesh

## Slide 28
NETMESH
The baseline the load tests need
Network Testing at Fleet Scale
28
netmesh
IDLE: latency · loss · path MTU
→
iperf-orchestrator
LOADED: TCP bandwidth
→
mx
LOADED: packets per second
▪ The load tools tell you what the fabric can *carry*. netmesh tells you what the fabric is *like* when nothing is running — and every loaded number has to be read against that baseline.
▪ It measures round-trip time, jitter, loss and path MTU between your machines, using ~10 small packets per second per pair — light enough to run on production, during an incident.
▪ Two hosts and one line is the whole experience: netmesh check web01 db01.
Notes: The one-sentence pitch: a 9.4 gigabit result over a 300-microsecond path and the same result over a 42-millisecond path are different results — netmesh is how you know which one you have. It's also the tool to reach for first in an incident, because it's the only one of the three that's safe to point at production while users are on it.

## Slide 29
NETMESH
Why not just ping?
Network Testing at Fleet Scale
29
▪ netmesh probes with small UDP packets between two tiny agents it places on your hosts — which buys four things ping can't do:
 | ping | netmesh
Privileges | often needs root / special settings | none — ordinary sockets, ordinary user
Latency | approximate | exact — the sender's own clock stamp comes back in the echo
Loss | one number, no direction | split: *on the way there* vs *on the way back*
Path measured | the router's management CPU — rate-limited, it lies | the same path your application traffic takes
▪ One-way delay is deliberately not reported: without synchronized clocks it would be a made-up number, and this tool doesn't report those.
Notes: For endpoints you can't put an agent on — a VIP, a router, an appliance — prefix the host with ~ and it falls back to ping, but those rows are clearly quarantined in the report as one-sided, because they carry less truth. The theme continues: every number quoted is one that is actually true.

## Slide 30
NETMESH
Reading the report
Network Testing at Fleet Scale
30
Finding | How to read it
Headline | the *median* pair's latency — one sick pair can't drag it or hide in it; worst pairs listed below
Asymmetry | A→B slow, B→A fine → look at A's *sending* side: the return trip proved the rest of the path
MTU black hole | small packets pass, big ones silently vanish — "small requests work, large transfers hang"
Path spread | one stream 29× slower than its siblings = a sick member inside a LAG/ECMP bundle
Under load | what the load *did* to latency: p99 210 µs idle → 42 ms loaded is what everyone else paid
▪ And a clean run says so in plain words: "the network is not your problem."
Notes: Every diagnosis is computed from the data, not canned: slow pairs sharing a source point at that host's egress; sharing a destination, its ingress; crossing a rack boundary, the path between. The under-load section is the bridge back to the other two tools — wrap netmesh around an iperf or mx run and the latency cost of the throughput number appears in the same report.

## Slide 31
NETMESH
Following up on what it finds
Network Testing at Fleet Scale
31
▪ A sick pair? netmesh paths --compare web03:db01 web01:db01 — prints the two routes side by side and marks the first hop where they differ. That hop is where to look.
▪ A clean baseline? Then the network isn't your problem — go load it: iperf-orchestrator all, mx run.
▪ A host that's still slow? Check the box itself before blaming the network again.
▪ Cleanup is automatic for check (it removes everything it deployed); for managed runs, stop keeps the reports and clean verifiably removes every trace.
Notes: The comparison trick in paths --compare is the practical gem: a sick route diffed against a healthy one turns "somewhere in the fabric" into "this hop". And the report itself tells you when to stop debugging the network — a clean baseline pointing you at the load tools closes the loop of the talk.

## Slide 32
NETMESH
Tutorial — netmesh in five minutes
Network Testing at Fleet Scale
32
# 0. prove the machinery works -- loopback only, no ssh needed
netmesh selftest
# 1. the two-host check: deploy, probe, report, clean up
netmesh check web01 db01
netmesh check web01 db01 --for 60 # a longer look
# 2. hunting a fault that comes and goes: sweep the paths
# inside a LAG/ECMP bundle
netmesh check web03 db01 --flows 8
▪ check leaves nothing behind — it deploys its agents, probes, prints the report and cleans up after itself.
▪ The report ends with *what to do next*, including "the network is not your problem" when that's the truth.
Notes: selftest first is the confidence builder — two agents over loopback, no second machine, no privileges. Then the two-host check is genuinely the whole experience for most users; --flows is the flag to remember when a fault reproduces only sometimes, because which bundle member you hash onto is luck until you sweep.

## Slide 33
NETMESH
Tutorial — repeat runs and load testing
Network Testing at Fleet Scale
33
# a standing mesh you can re-run
netmesh gen --servers prod.txt
netmesh run --for 300 --grid grids/ # 5 minutes + N x N grids
# measure what a load test does to latency:
# 20 s idle baseline, then keep probing while the load runs
netmesh run --baseline 20 -- ./iperf_orchestrator.sh all
# a sick pair? find the hop where its route diverges
netmesh paths --compare web03:db01 web01:db01
netmesh clean # managed runs: verified removal
▪ Same verbs as mx (gen / start / status / summarize / stop / clean) and the same grid format — learn one, know both.
▪ In every report, blank means "not measured" — never zero.
Notes: The --baseline wrapper is the closing move of the whole talk: baseline, then load, one report showing both. Grids land next to mx's grids in the same spreadsheet. And the honesty rule one last time — a pair that stopped answering writes blanks, because averaging zeros in would flatter the baseline, and a baseline tool must never flatter.

## Slide 34
WRAP-UP
Close

## Slide 35
WRAP-UP
Putting it together
Network Testing at Fleet Scale
35
reachable
keep the list real
→
netmesh
idle baseline
→
iperf-orchestrator
TCP bandwidth
→
mx
packets per second
→
netmesh --baseline
latency under load
▪ 1 · Start with the list — reachable prod.txt -i comments out dead servers, so every later step measures the fleet, not the list.
▪ 2 · Baseline while idle — netmesh check gives the latency, loss and MTU numbers every later result is read against. Safe on production.
▪ 3 · Load it with bytes — iperf-orchestrator all floods every link both ways: the bandwidth ceiling, and the first look at what breaks.
▪ 4 · Load it with packets — mx run finds the answered-packets-per-second ceiling: the shape of real RPC and storage traffic.
▪ 5 · Measure the cost — wrap netmesh around a load run to see what the load did to latency for everyone else on the path.
▪ Three habits: baseline before load · trust what arrived, not what was sent · keep the list real.
Notes: Walk the flow left to right, one sentence per box — it's the whole talk replayed in thirty seconds. Each stage's answer is the context for the next: a pruned list makes the baseline trustworthy, the baseline makes the load numbers readable, and the two load ceilings — bytes and packets — bracket what the fabric can really do. The last box closes the loop: throughput always has a latency price, and measuring it is one wrapper command. Everything installs with pip; netmesh and reachable ship together in one package alongside the two orchestrators.